## Slide 1: Atmospheric Correction Intercomparison eXercise (ACIX-Aqua)
Nima Pahlevan / SSAI
NASA Goddard Space Flight Center / Code 619
ACIX-Aqua
Dense Microcystis bloom - West Sister Island (Lake Erie) 09/27/2014

## Slide 2: Product Developments
Universal algorithms (through a community-wide data sharing activity)
Chlorophyll-a retrievals for Sentinel-2/3 (MDN)
Pahlevan et. al. (2020). Seamless retrievals of chlorophyll-a from Sentinel-2 (MSI) and Sentinel-3 (OLCI) in inland and coastal waters: A machine-learning approach. Remote Sensing of Environment, 240, 111604. source code: https://github.com/BrandonSmithJ/MDN
N ~ 2700
TSS/SPM/TSM retrievals (SOLID)
Balasubramanian, et. al.. (2020). Robust Algorithm for Estimating Total Suspended Solids (TSS) in Inland and Nearshore Coastal Waters. Remote Sensing of Environment, 111768. source code: https://github.com/BrandonSmithJ/MDN/tree/master/Benchmarks/tss/SOLID

## Slide 3: ACIX-Aqua: Objective
ACIX-Aqua
Provide guidance for global production of aquatic science products from Landsat (OLI) /Sentinel-2 (MSI) missions
  Identify strengths/weaknesses of atmospheric correction (AC) processors
  Inform users/agencies of the performances

## Slide 4
Processing Team:
from various Space Agencies, R&D Companies,
Research Institutes
and Universities
8
15
Initial report
Work in progress to publish the results
Dec 2019
# of valid matchups
with Sentinel-2A/B, and Landsat-8
500
+ 700
ACIX-Aqua: General Info
ACIX-Aqua
Data Team:
AERONET-OC data (Phase I)
+ Freshwater data (Phase II)

## Slide 5: Matchups (geographic distribution)

## Slide 6
OLI & MSI combined
Performance Assessment ()

## Slide 7
MSI data
Performance Assessment ()

## Slide 8
How Propagates to Products?
  Sample products
    Chlorophyll-a (Chla) & Total Suspended Solids (TSS)
  Two possible approaches
    Quantitative: use common matchups (n ~ 140) among AC processors
    Qualitative: use in situ radiometric spectra to generate pseudo Chla and TSS measurements. The estimated Error and Bias metrics are therefore denoted by {Error} and {Bias}

## Slide 9: Impacts on Downstream Products: OLI-derived Chla (Freshwater)
Satellite retrievals [mg/m3] (log scale)
Pseudo Chla [mg/m3] (log scale)
Pseudo products are derived from the MDN model:
Pahlevan et. al. (2020). Seamless retrievals of chlorophyll-a from Sentinel-2 (MSI) and Sentinel-3 (OLCI) in inland and coastal waters: A machine-learning approach. Remote Sensing of Environment, 240, 111604.

## Slide 10: Impacts on Downstream Products: MSI-derived Chla (Freshwater)
Satellite retrievals [mg/m3]
Pseudo Chla [mg/m3]
Pseudo products are derived from the MDN model:
Pahlevan et. al. (2020). Seamless retrievals of chlorophyll-a from Sentinel-2 (MSI) and Sentinel-3 (OLCI) in inland and coastal waters: A machine-learning approach. Remote Sensing of Environment, 240, 111604.

## Slide 11: Impacts on Downstream Products: OLI-derived TSS (AERONET-OC)
Satellite retrievals [g/m3]
Pseudo TSS [g/m3]
Pseudo products are derived from the SOLID model:
Balasubramanian, et. al.. (2020). Robust Algorithm for Estimating Total Suspended Solids (TSS) in Inland and Nearshore Coastal Waters. Remote Sensing of Environment, 111768.

## Slide 12: Conclusion
With 20-30% uncertainties in , estimated uncertainties in Chla and TSS products are 40-70%
ACIX-Aqua
Possible pathways forward
  Machine-learning models are promising
  Incorporate more representative (land) aerosol models

## Slide 13
Partner Institutions
  Krista Alikas (Tartu Observatory; Estonia)
  Caren Binding (ECCC; Canada)
  Ronghua Ma (NIGLAS; China)
  Daniela Gurlin (Wisconsin DNR)
  Wesley Moses (NRL)
  Moritz Lehmann (U of Waikato, New Zealand)
  Nguyen Ha (VNU; Vietnam)
  Hubert Loisel (ULCO, LOG, France)
  Mike Ondrusek (NOAA, MD)
  John Schalles (U Creighton, NE)
  Leif Olmanson (U Minnesota, MN)
  Korean Institute of Ocean Science and Technology (KIOST)
  Bunkei Matsushita (University of Tsukuba, Japan)
  Cedric Fichot (Boston U, MA)
  David O’Donnell (UFI, NY)
  Steve Ruberg (NOAA GLER, MI)
  Lin Li (Indiana U - IUPUI)
  Tristan Harmel (GE, France)
  Yannick Huot (U Sherbrooke, Canada)
  Evangelos Spyrakos (U of Stirling; U.K.)
  Steef Peters (Water Insight; Netherlands)
  Mark Warren (Plymouth Marine Laboratory, U.K.)
  Claudia Giardino (CNR, Italy)
  NASA PIs (SeaBASS)

## Slide 14: Backup

## Slide 15
Data Team
  Krista Alikas (U Tartu; Estonia)
  Claudio Barbosa/Lino Augusto (Brazil)
  Caren Binding (ECCC; Canada)
  Ronghua Ma (NIGLAS;China)
  Claudia Giardino / Mariano Bresciani (CNR; Italy)
  Daniela Gurlin (Wisconsin DNR)
  Yannick Huot/Simon Bélanger (Canada)
  Moritz Lehmann (U of Waikato; New Zealand)
  Nguyen Ha (VNU; Vietnam)
  Tristan Harmel (Géosciences Environnement Toulouse)
  Leif Olmanson (U of Minnesota; U.S.)
  Natascha Oppelt (U of Kiel; Germany)
  Steef Peters (Water Insight; Netherlands)
  Evangelos Spyrakos (U of Stirling; U.K.)
  Mark Warren (Plymouth Marine Laboratory, U.K.)
Processing Team (AC processor)
  Quinten Vanhellemont (ACOLITE)
  Kerstin Stelzer (C2X)
  Tristan Harmel (GRS)
  Antoine Mangin (MeetC2)
  Yongzhen Fan (OCSMART)
  François Steinmetz (POLYMER)
  Nima Pahlevan (SeaDAS)
  Sindy Streckx (iCOR)
ACIX-Aqua
Support Team
  Sundarabalan Balasubramanian (NASA GSFC Team)
  Christophe Bevy (ESA /ACRI Team)

## Slide 16
CONCLUSIONS
  Although some of the processors suggest promising results, they appear to yield inaccurate aquatic reflectance products ( > 20%) when robust retrievals across VNIR bands are desired
  Research efforts for improving the performances are encouraged
  Improvements will be made given lessons learned via ACIX-Aqua
SUGGESTIONS
  Teams should highlight strengths of their processors.
  Teams should evaluate dependency on geometry, environmental conditions, adjacent land, etc.
  Current assessment is preliminary, and feedback is sought for improving the analysis.
DISCUSSION
  Can we reach a consensus on uncertainty requirements by evaluating the corresponding impacts on downstream products?
ACIX-Aqua

## Slide 17
Impacts on downstream products (tentative plan) – Analyze errors in Chla and SPM retrievals induced by AC
Freshwater
  Reference set: Some in situ measured Chla & SPM are available (MEASURED). For the rest, Chla & SPM can be estimated well from hyperspectral (IDEAL)
  Estimate Chla & SPM from simulated OLI and MSI (PRACTICAL) – What is possible via OLI and MSI if there were no uncertainties in AC?
  Estimate Chla & SPM from through different AC methods (RETRIEVED)
AERONET-OC
  Reference set: Estimate Chla & SPM from AERONET-OC products ()
  Estimate Chla & SPM from simulated OLI and MSI obtained from AERONET-OC products ()
  Estimate Chla & SPM from through different AC methods (RETRIEVED)
ACIX-Aqua

## Slide 18
Questions?
Start
1st ACIX II-CMIX workshop
Oct 2018
Nov 2019
Submission to CTEP AERONET-OC
Phase I
March 2019
Inter-comparison Analysis
2nd ACIX workshop
Initial
Report Release 2nd ACIX workshop
May 2020
Report (MS 1)
Submission to Scientific Journal
ACIX-Aqua
Dec 2019
Sep 2019
Product Extraction
Results Submission
May 2019
Submission to CTEP Phase II
Sep 2020
Report (MS 2)??
Submission to Scientific Journal
Notes: Teams with large databases or those expecting to collect more data early Spring can provide portions of their data until early June next year.
Living Planet Symposium 2019 (May).