## Slide 1: Suomi National Polar-orbiting Partnership (NPP) VIIRS data product assessment
K. Turpie
Ocean Color Science PI
VIIRS Ocean Science Team (VOST)
Ocean Color Research Team Meeting
23 April 2012
Seattle, Washington
Notes: Shown is Jyväskylä University.

## Slide 2
Robert Barnes
Gene Eplee
Gwyn Fireman
Bryan Franz, Co-I
Chuck McClain, Admin PI
Gerhard Meister
Fred Patt, PEATE Tech Lead
Wayne Robinson
VIIRS Ocean Science Team (VOST)
2

## Slide 3
VOST Efforts
The VIIRS Instrument
VIIRS Data Features
VOST Calibration
Initial Results
Conclusions
Table of Contents
3
5
12
20
24
29
33

## Slide 4
5:48 EDT 28 October 2011
4
Since the last OCRT Meeting
Suomi NPP Successfully Launched!

## Slide 5: VOST Efforts
5

## Slide 6
VOST Contributions 2003-Present
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
6

## Slide 7
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
VOST Contributions 2003-Present
Blocking Earth shine thru the calibrator screen
Clear water calibration site
Lunar calibration maneuvers
Significant reduction of optical crosstalk
End-to-end calibration system test
Spectral response characterization with SIRCUS
Characterization of crosstalk polarization effects
Improved polarization response characterization
7

## Slide 8
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
VOST Contributions 2003-Present
Ocean color sensitivity analysis techniques
Crosstalk impact analysis
VIIRS Data Simulator
  Predict impact of instrument effects.
  Prepare team for flight data.
  Exercise processing system prelaunch.
8

## Slide 9: Product Quality Assessment
VOST Question: Is the quality of the operational VIIRS Ocean Color Environmental Data Records (EDR) sufficient to meet NASA science objectives, including the continuation of the climate record established with EOS?
Approach: Evaluate prelaunch sensor characterization, algorithms, calibration and processing capabilities and compare EDR products against products generated with NASA calibration and algorithms.
Answer: Unlikely. Sensor appears to be performing well, but :
EDR algorithms are out of date and inconsistent with established record,
calibration is forward-looking only, and
there is no support for reprocessing.
Also precludes processing from Sensor Data Records (SDR).
9

## Slide 10: Product Quality Assessment
OBPG Question: Is the current quality of the VIIRS Raw Data Records (RDR) sufficient for meeting NASA science objectives, including the continuation of the climate record established with EOS?
Approach: Evaluate results of reprocessing VIIRS sensor measurements using NASA standard algorithms and time-dependent calibration.
Preliminary Answer: Likely. So far, there are no insurmountable problems with VIIRS sensor measurements and reprocessing with NASA calibration and algorithms initially appears to produce ocean color products roughly comparable to SeaWiFS climatology.
10

## Slide 11: Product Quality Assessment
VOST Future: To further quantify how closely (or not) operational EDR products meet NASA's science objectives, the VOST will compare them against :
flight data reprocessed with NASA time-dependent calibration and algorithms,
the established CDR (cross sensor and climatology), and
in situ data.
OBPG Future: To quantify how well the VIIRS sensor measurements meet NASA’s science objectives, the OBPG will retrospectively compare the more refined NASA-generated VIIRS data record to :
the established CDR (cross sensor and climatology), and
in situ data.
11

## Slide 12: The VIIRS Instrument
12

## Slide 13
PURPOSE: Global operational observations of land, ocean, & atmosphere parameters.
PREDECESSORS: AVHRR, OLS, MODIS, SeaWiFS
FACT SHEET
Multi-spectral crosstrack scanning instrument
Rotating telescope design, similar to SeaWiFS
Flies on Suomi NPP and every JPSS satellite
Imagery and radiometry
  Imaging band at 0.4 km resolution (nadir)
  Radiometric bands at 750m resolution
  12 bit quantization
  Some bands have high and low gain modes
22 spectral bands (0.4 – 12.5 μm)
  15 “reflective” VNIR-SWIR bands 0.4 – 2.3 μm
  3 “mixed” MWIR bands 3.5 – 4.1 μm
  4 “emissive” LWIR bands 8.4 – 12.5 μm
  Automatic dual VNIR & triple DNB gains
Maximum swath width
  3000 km
13
VIIRS OVERVIEW

## Slide 14: VIIRS Features
SWIR
NIR
Visible
Ultraviolet
No Measurements
CZCS
SeaWiFS
MODIS
VIIRS
14
Characteristic | SeaWiFS | MODIS | VIIRS
Band Set (nm) | 412, 443, 490, 510, 555, 670, 765, 865 | 412, 443, 488, 531, 547, 667, 678, 748, 869 | 412, 445, 488, 555, 672, 746, 865
Nadir Pixel Size | 1.1 km | 1 km | 0.75 km
SNR Range | 364 to 1010 | 726 to 2219 | 540 to 1239
Polarization Sensitivity | < 0.25% (Vis) < 0.5% (NIR) | 1% to 6% | 0.5% to 2.5%
Out-of-Band (worst case) | 5.7% @865nm | 3.8% @748 nm | 4.9% @551 nm
Crosstalk? | None | SWIR | VisNIR
Tilt | -20,0,+20° | 0° | 0°
Detectors per Scan | 1 | 10 | 16

## Slide 15: VIIRS Features
Characteristic | SeaWiFS | MODIS | VIIRS
Band Set (nm) | 412, 443, 490, 510, 555, 670, 765, 865 | 412, 443, 488, 531, 547, 667, 678, 748, 869 | 412, 445, 488, 555, 672, 746, 865
Nadir Pixel Size | 1.1 km | 1 km | 0.75 km
SNR Range | 364 to 1010 | 726 to 2219 | 540 to 1239
Polarization Sensitivity | < 0.25% (Vis) < 0.5% (NIR) | 1% to 6% | 0.5% to 2.5%
Out-of-Band (worst case) | 5.7% @865nm | 3.8% @748 nm | 4.9% @551 nm
Crosstalk? | None | SWIR | VisNIR
Tilt | -20,0,+20° | 0° | 0°
Detectors per Scan | 1 | 10 | 16
SWIR
NIR
Visible
Ultraviolet
No Measurements
CZCS
SeaWiFS
MODIS
VIIRS
VIIRS SNR here is based on typical Lt for ocean.
Noise averaged over all six aggregation zones.
Overall, noise levels are comparable to SeaWiFS, 3:1 agg zone having better SNR.
15

## Slide 16: VIIRS Features
Characteristic | SeaWiFS | MODIS | VIIRS
Band Set (nm) | 412, 443, 490, 510, 555, 670, 765, 865 | 412, 443, 488, 531, 547, 667, 678, 748, 869 | 412, 445, 488, 555, 672, 746, 865
Nadir Pixel Size | 1.1 km | 1 km | 0.75 km
SNR Range | 364 to 1010 | 726 to 2219 | 540 to 1239
Polarization Sensitivity | < 0.25% (Vis) < 0.5% (NIR) | 1% to 6% | 0.5% to 2.5%
Out-of-Band (worst case) | 5.7% @865nm | 3.8% @748 nm | 4.9% @551 nm
Crosstalk? | None | SWIR | VisNIR
Tilt | -20,0,+20° | 0° | 0°
Detectors per Scan | 1 | 10 | 16
SWIR
NIR
Visible
Ultraviolet
No Measurements
CZCS
SeaWiFS
MODIS
VIIRS
Apparatus used to characterize MODIS and VIIRS polarization response was abandoned.
Rotated polarizer sheets were used instead; similar to method used for SeaWiFS.
Resulting characterization for VIIRS polarization response was much better quality than what was done for MODIS.
16

## Slide 17: VIIRS Features
Characteristic | SeaWiFS | MODIS | VIIRS
Band Set (nm) | 412, 443, 490, 510, 555, 670, 765, 865 | 412, 443, 488, 531, 547, 667, 678, 748, 869 | 412, 445, 488, 555, 672, 746, 865
Nadir Pixel Size | 1.1 km | 1 km | 0.75 km
SNR Range | 364 to 1010 | 726 to 2219 | 540 to 1239
Polarization Sensitivity | < 0.25% (Vis) < 0.5% (NIR) | 1% to 6% | 0.5% to 2.5%
Out-of-Band (worst case) | 5.7% @865nm | 3.8% @748 nm | 4.9% @551 nm
Crosstalk? | None | SWIR | VisNIR
Tilt | -20,0,+20° | 0° | 0°
Detectors per Scan | 1 | 10 | 16
SWIR
NIR
Visible
Ultraviolet
No Measurements
CZCS
SeaWiFS
MODIS
VIIRS
Similar to worse cases for SeaWiFS or MODIS.
The blue light leak in the green band is the greatest concern, as shown above.
OUT-OF-BAND LIGHT LEAKS
17

## Slide 18: VIIRS Features
Characteristic | SeaWiFS | MODIS | VIIRS
Band Set (nm) | 412, 443, 490, 510, 555, 670, 765, 865 | 412, 443, 488, 531, 547, 667, 678, 748, 869 | 412, 445, 488, 555, 672, 746, 865
Nadir Pixel Size | 1.1 km | 1 km | 0.75 km
SNR Range | 364 to 1010 | 726 to 2219 | 540 to 1239
Polarization Sensitivity | < 0.25% (Vis) < 0.5% (NIR) | 1% to 6% | 0.5% to 2.5%
Out-of-Band (worst case) | 5.7% @865nm | 3.8% @748 nm | 4.9% @551 nm
Crosstalk? | None | SWIR | VisNIR
Tilt | -20,0,+20° | 0° | 0°
Detectors per Scan | 1 | 10 | 16
SWIR
NIR
Visible
Ultraviolet
No Measurements
CZCS
SeaWiFS
MODIS
VIIRS
Similar to worse cases for SeaWiFS or MODIS.
The blue light leak in the green band is the greatest concern, as shown above.
OPTICAL CROSSTALK
18

## Slide 19
Mirrors contaminated WO3(?) during manufacture.
Causes severe, progressive loss in NIR and SWIR bands response when exposed to UV.
Testing with witness samples suggest worst case of 30% lost in 895 nm band (M7).
Mirror Degradation
19
NAD Open
Might impact ocean color data quality at some point in the mission.
However, while the instrument is operating normally, the resulting degradation is smooth and trackable.
Early lunar measurements show strong agreement solar diffuser calibration (see plots on calibration slides).

## Slide 20: VIIRS Data Features
20

## Slide 21
1- some granules on contain 47 scans.
2- OBPG eval prods are in HDF4 format; conventions same as MODIS and SeaWiFS.
3- OPBG L0-L3 eval prods available via OC website.
VIIRS Features
RDR = L0
SDR = L1b
EDR = L2
? = L3*
* There is no operational equivalent to L3
Granule Feature | MODIS | S-NPP VIIRS
Sun Sync Orbit | Terra – Descending Aqua – Ascending | Ascending
Equator Crossing Time | Terra – 1030 Aqua – 1330 | 1330
Altitude (km) | 705 | 824
Scan Coverage (km) | 2330 | 3000
Time Coverage | 5 mins | 85.4 secs
No. of Scans | 203 | 481
No. Dets per Scan | 10 (Mod res) | 16 (Mod res)
Aggregation Zones | None | 6 (3 types)
Data Format | HDF4 | HDF52
L1 Data Band Org | Separate SDS’s | Separate Files
Data Distribution | OC Website | CLASS3

## Slide 22
2:1
1:1
3:1
2 edge detectors removed
4 edge detectors removed
1
2
3
4
5
6
22

## Slide 23
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
1
2
3
4
5
6
56o
43.6o
32o
32o
43.6o
56o
nadir
1500km
850km
530km
530km
850km
1500km
three 250m samples per pixel
two 250m samples per pixel
no aggregation
bow-tie
deletion
Scan Aggregation Zones
Dual-gain Bands - samples aggregated on ground.
Singe-gain Bands - samples aggregated on-board (only M6 for ocean bands).
source: MDFCB, 4 Nov 2004
The Anatomy of a VIIRS Scan
23

## Slide 24: VOST Calibration
24

## Slide 25: Solar Calibration
VOST pre-launch counts-to-radiance conversion uses linearization of ATBD eqns.
Solar Diffuser (SD) is used to track changes in instrument response from prelaunch.
SDSM tracks changes in SD. (Quis custodiet ipsos custodes?)
VOST developed a time-dependent capability to support reprocessing.
25

## Slide 26: Lunar Calibration
Lunar calibration - Successful measurements :
  partial bands in Jan (412 & 443 nm bands were clipped),
  Jan serendipitous measurements for 412, 443, and 488 nm bands,
  dual rolls in Feb (measured all bands in VisNIR and SWIR),
  missed in Mar but got serendipitous for seven bands (green, red, 2 NIR, and 3 SWIR), and
  sector rotation in Apr; captured and co-registered all bands.
Next measurement is scheduled for the 2 May.
Measurements verify the solar cal and can replace it if need be later in the mission.
Can incorporate lunar measurement trending in calibration after at least one year of acquisitions.
26

## Slide 27
27
551 nm
670 nm
750 nm
865 nm
Days since 1 Jan 2012
-50
0
50
100
0.75
0.80
0.85
0.90
0.95
1.00
Relative Response
Normalized Lunar Cals
Stabilized Calibration Data
NASA VIIRS SOLAR CALIBRATION
with Verification OF Lunar Measurements

## Slide 28
412 nm
443 nm
488 nm
551 nm
Days since 1 Jan 2012
-50
0
50
100
0.98
0.99
1.00
1.01
Relative Response
Normalized Lunar Cals
Stabilized Calibration Data
28
NASA VIIRS SOLAR CALIBRATION
with Verification OF Lunar Measurements

## Slide 29: Initial Results
29

## Slide 30: VIIRS & MODIS Aqua Deep-Water Rrs Trends NASA Calibration and L2 Processing
30
solid line = MODIS Aqua (updated OBPG calibration)
dashed = VIIRS (preliminary OBPG calibration)
Temporal stability is comparable biases to be resolved through vicarious calibration.
Rrs (sr-1)

## Slide 31
31
We can reproduce the AOT trends we get from Aqua.
Demonstrates that the NIR calibration is on track.
VIIRS Deep-Water Aerosol Optical Thickness Trends IDPS L1Bs vs OBPG L1Bs, Both with NASA L2 Processing
solid line = MODIS Aqua (updated OBPG calibration)
dashed = VIIRS (preliminary OBPG calibration)

## Slide 32: VIIRS & MODIS Aqua Deep-Water Chl NASA VIIRS L2, EDR, & MODIS Aqua
NPP VIIRS L2 Chl
Aqua MODIS Chl (Deep Water)
NASA calibration, L2 algorithms, and flags
Composite: Day 73-81
32
NPP VIIRS EDR Chl
NOAA calibration, EDR algorithms, and flags
VIIRS L2 and EDR are comparable in range distribution to updated MODIS Aqua.
EDR differences are visible.
  Flags present differences.
  Calibration may dominate differences
Composite: Day 73-80

## Slide 33: Conclusions
VOST has invested several years of effort working with NPP VIIRS.
NPP VIIRS is currently performing well; performance anomalies are correctable.
Generating NASA VIIRS evaluation products to answer VOST and OBPG questions.
  NASA evaluation products are based on same L2 algorithms used to generate NASA science and climate quality datasets from SeaWiFS and MODIS.
  Implemented a time-dependent calibration strategy based on solar diffuser and lunar measurements.
  Generating L3 products to support comparisons (there is no operational L3 product).
33

## Slide 34: Conclusions
EDR products cannot be evaluated prior to 6 Feb; quality too poor. (VOST Question)
Evaluation can begin now that sufficient EDR data has be collected. (VOST Question)
With NASA calibration and processing, the VIIRS products are qualitatively comparable in dynamic range and stability to SeaWiFS climatology based on a limited time series.
Early mission assessment suggests that application of a time-dependent calibration and common algorithms to VIIRS sensor measurements could continue the EOS climate data record. (OBPG Question)
34

## Slide 35: Kiitos paljon!

## Slide 36
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
VOST Contributions 2003-Present
Instrument Requirements
Waiver Requests
Characterization Test Plans
Test Analysis Reports
Contractor Anomaly Impact Analysis Reports
Theoretical Basis
Product Performance Specifications
Data Format and Interface Specifications
36

## Slide 37
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
VOST Contributions 2003-Present
Identified coding errors.
Provided sun glint correction code.
Noted NASA improvements that were missing:
  NIR correction,
  Improved aerosol models,
  Revised whitecap correction,
  BRDF correction,
  Band pass adjustments, and
  Chl based on Carder algorithm.
37

## Slide 38
VOST Contributions 2003-Present
Reviewed numerous project documents
Reviewed science and operational code
Successfully advocated instrument improvements
Performed multiple analyses of the effect instrument performance on data quality
Presented findings at numerous technical conferences
Participated in test planning and data analysis
VIIR ocean color data product quality assessment
Development of time-dependent calibration
Generation of VIIRS data products using NASA algorithms
38

## Slide 39
Impact analysis for ocean color showed showed much smaller effect.
NGC decides to correct optical X-talk using OOB techniques.
Severe X-talk discovered in EDU.
Dynamic X-talk addressed in flight unit.
Innovative testing was designed to fully characterize optical X-talk.
NIST SIRCUS is used to characterize VIIRS spectral response.
Testing showed small optical X-talk but large OOB light leaks !!!
Hybrid spectral response tables use for correction of OOB and X-talk
Optical X-talk in flight unit found to be lesser but still significant.
Raytheon flips the filters in the flight unit.
Hybrid spectral response implemented in NASA L2 code.
2006
2007
2010
2011
2012
2009
2008
THE RISE AND FALL OF THE CROSSTALK ISSUE
39
Notes: We saw at look of crosstalk, vendor flipped IFA, this caused a tradefoff between xtalk and OOB

## Slide 40
24 Mar 2012
Petulant Mode
Event
(Cold focal plane warms)
Cryo-radiator activated
40
1260 nm
1360 nm

## Slide 41
NAD Open
41

## Slide 42
SDSM Measurements are normalized to det 8 to remove spurious signal.
Calibration uses NICSE’s new SDSM screen transmission table based on measurements taken during yaw maneuvers.
42

## Slide 43
43

## Slide 44
RDR (L0)
Files
ADL
SDR (L1b)
Files
Static
Cal
Tables
F Table
F Table
Preproc
f Time
Series
H Time
Series
TS
Trending
TS
Generator
RDR
Cal Pool
Cal RDR
Selection
Script
SD BRDF
SDS t
SDSMS t
Geo
Cal
Tables
Polar
Wander
File
Off-line Solar Cal
F History
w/ Extra-
polation
F History
Generator
F History
Table
L1 Production Process
44

## Slide 45
NPP VIIRS Chl
Aqua MODIS Chl
NASA calibration and L2 algorithms
Composite: Day 73-81
Composite: Day 73-81
NOAA EDR
NASA Chl
NASA Chl
Horizontal stripes caused by bow-tie deletion
EDR has additional pixel trimming
Projections of the above VIIRS and MODIS
swath cutouts projections are different.
10 Feb 2012 (Day 41)
10 Feb 2012 (Day 41)
10 Feb 2012 (Day 41)
45
0.01 – 1.0 mg m-3

## Slide 46: Vicarious Calibration
Vicarious calibration
  Initially based on Ocean Surface Reflectance Model using HOT and BATS sites.
  Will use surface values later in the mission, e.g., MOBY (depending on availability and quality).
46